## Slide 1
Sous-titre ou nom de la personne
Titre de la présentation sur 2 lignes de texte maximum
BrightCon - September 24th, 2026
Matthieu Souttre, Guillaume Majeau-Bettez, François Maréchal, Manuele Margni
mescal
A Python package for coupling Life-Cycle Assessment with Energy System Models

## Slide 2: Table of contents
Basics about Energy System Models (ESMs)
Purpose and goals of mescal
Main input data and methods of mescal
Hands-on

## Slide 3: Typical structure of a technology-rich and optimization-based ESM
Technologies
Fossils and renewables Investment and O&M cost Efficiencies, emissions Storage
Resources (imports)
Cost & emissions Yearly availability
Energy demand
Energy strategy
Technology sizing and operation
Centralized vs decentralized heat supply
Public vs private mobility
Freight vs road
Optimization
Minimize
subject to:
- mass & energy balance - storage
Technology
Technology
Technology
Technology
Technology
Technology
Optimization variables
Infrastructures
Typically, ESMs are limited to direct CO2 emissions
 Overlooking indirect emissions and other environmental issues
 Coupling with LCA to fill these gaps

## Slide 4: Purpose and goals of mescal

## Slide 5: Purpose and goals of mescal
Couple () Energy System Models (ESMs) with LCA
 Endogenously integrate LCA metrics in ESMs
Why? For LCA metrics to play an active role in the generation of energy transition scenarios.
 Feed the ESMs results back in the LCI database (ecoinvent/premise)
Why? To connect the new energy transition scenarios with the rest of the supply chain.
Systematic and easy-to-apply methodology
Applicable to any bottom-up (technology-rich) ESM and with any set of LCIA methods
Compatible with other brightway-based tools (e.g., premise, regioinvent, etc.) that enrich the LCI database

## Slide 6: Integrating LCA impact scores in ESMs…
and feed the results back in the database
Notes: Regionalization = adapt LCI datasets to a given ESM geography
Double-counting = in LCI datasets, remove flows that are both in the ESM and in LCI datasets (e.g., energy flows)
Harmonization = align the technological parameters of technologies in ESM and LCI datasets (e.g., efficiency, lifetime, capacity factors, etc.)

## Slide 7: Main input data and methods of mescal

## Slide 8: Integrating LCA impact scores in ESMs…
and feed the results back in the database

## Slide 9: Mapping between ESM technologies/resources and LCI datasets
PV
photovoltaic slanted-roof installation, 1.3 MWp, multi-Si, panel, mounted, on roof (/unit)
electricity production, photovoltaic, at 1.3 MWp slanted-roof, multi-Si, panel, mounted (/kWh)
Infrastructure LCI dataset
Operation LCI dataset
ESM
LCA
COAL
market for hard coal (/kg)
Resource LCI dataset
ecoinvent / premise / regioinvent
We have done this (painful) step for every technology and resource in our ESM (EnergyScope), feel free to reuse this work!

## Slide 10: Integrating LCA impact scores in ESMs…
and feed the results back in the database

## Slide 11: Aligning physical units and other assumptions between ESM and LCA
Example with the infrastructure LCI dataset of any kind of car or truck:
BEVs in LCI database  [unit] as a functional unit (i.e., 1 car, 1 truck)
BEVs in ESM  [Mpkm/h] or [Mtkm/h] for installed capacities
In this case, we need the following assumptions from the LCI dataset :
Number of people per car (p) or load factor (t)
Annual distance (km/year)
8760 * capacity factor (hours/year)
Other technological parameters aligned by mescal:
lifetime, energy efficiency

## Slide 12: Aligning the energy efficiency
Problem: in case energy efficiencies are not aligned, inconsistencies might arise between fuel consumption (ESM) and direct emissions (LCA).
Boiler
Natural gas
Heat
ESM
1 kWh
2 kWh
Efficiency = 1 / 2 = 50%
If the efficiency in the LCI dataset is 33%, direct emissions are multiplied by 33/50
Boiler
Heat
Direct emissions
Natural gas
Lubricating oil
Manufacturing
3 kWh
1 kWh
Life-cycle inventory database
x 33/50

## Slide 13: Integrating LCA impact scores in ESMs…
and feed the results back in the database

## Slide 14: Solving the double-counting problem
Problem: flows represented in the ESM are also represented in LCI datasets, therefore their impact is double-counted.
Boiler
Natural gas
Heat
Boiler
Heat
Direct emissions
Natural gas
Double-counting
ESM
Life-cycle inventory database
Lubricating oil
Manufacturing
Complementary inputs and emissions coming from LCA embodied in metrics to be integrated in the ESM
Correspond in the CPC mapping

## Slide 15: Integrating LCA impact scores in ESMs…
and feed the results back in the database

## Slide 16: Create new datasets based on ESM results
Method: considering production results, mescal builds new markets for all commodities represented in the ESM and connects them to the rest of the database. Example with electricity:
300 TWh/year
200 TWh/year
500 TWh/year
ESM results
New LCI dataset
Activity: market for electricity, high voltage
Reference product: electricity, high voltage (1 kWh)
Location: ESM location
Exchanges:
Electricity production, nuclear (0.5 kWh)
Electricity production, solar photovoltaic (0.3 kWh)
Electricity production, onshore wind (0.2 kWh)
Taken from the mapping file

## Slide 17: Integrating LCA impact scores in ESMs…
and feed the results back in the database

## Slide 18: Visualize your results
Basic bar plots to visualize LCA impact scores and system-level LCA results
Example : human health impact scores for a few energy resources

## Slide 19: Visualize your results
Basic bar plots to visualize LCA impact scores and system-level LCA results
Example : top 5 contributors in the system
More of mescal’s plots here

## Slide 20: Visualize your results
Advanced app for contribution analyses (processes and elementary flows)
Example: contribution analysis of elementary flows among energy resources for the category “total human health”
Streamlit app

## Slide 21: More details and how to cite
For more details and a funny case study, have a look at our publication:

## Slide 22: Installation and documentation
pip install mescal
https://pypi.org/project/mescal/
Github
https://github.com/matthieu-str/mescal
ReadTheDocs
https://mescal.readthedocs.io/en/latest/

## Slide 23
Merci!
Questions?
ciraig.org
Matthieu Souttre
Ph.D. student
Montréal - Canada
matthieu.souttre@polymtl.ca

## Slide 24: Equations
Notes: Time dimension  we allocate (1 / lifetime) of the impact of energy infrastructures being installed to the current year y.