## Slide 1: naKnow: a collaborative initiative to bridge data gaps in ICT life cycle assessment using parametric modelling
Thibault Simon1, Marie Reinbigler1, Anish Koyamparambath2, Arthur Removille1
1 Resilio
2 WeLOOP
Brightcon 2026

## Slide 2
Context
page <numéro>
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Eco-design and responsible innovation suffer from this situation:
Limited access to high-quality, component-level data
Information that is often outdated or incomplete
Knowledge that is fragmented and difficult to mobilize
naKnow addresses the lack of transparent, reliable, and actionable environmental intelligence for electronic components.

## Slide 3
page <numéro>
23/09/2026
naKnow is an international federating platform to build environmental intelligence for the electronics industry
We are a Swiss-Based
Non-Profit Association
A place for the actors of the electronics industry to share their challenges & find solutions together
Context
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 4
naKnow Association
page <numéro>
23/09/2026
LCA & methods expertise
Policy making and regulations
Ecodesign improvement
Supply chain impact
Reporting ESG
Knowledge creation and transmission
A network of experts in the industry, research and academia
Reliable collaborative LCA data
RESEARCH AND TECHNOLOGY ORGANISATION
ACADEMIA PLAYERS
INDUSTRY PLAYERS
PUBLIC BODIES
Provide environmental data expertise
DATABASES PROVIDERS
CONSULTANCIES
Provide data, research expertise and laboratory facilities
Global impact & ESG reporting improvement
HYPERSCALERS
01
ASSOCIATION GOVERNANCE
A board with diverse representation
02
OPEN KNOWLEDGE BASE
Reviewed and traceable knowledge
+
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 5
Overview of the Method
page 4
23/09/2026
support
testing
correction
comparison
EXISTING MODELS
PARAMETRIC LCA MODELS
LABORATORY EXPERIMENTS
LITERATURE RESEARCH
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Five components
Printed Circuit Board
Integrated Circuits
Optical Sensors
Hard Disk Drive
Screens
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 6
Data generation pipeline
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Litterature
Expert knowledge
YAML config files
Calculator
Impact characterization
LCIA data
Documented in the knowledge base
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 7
Collaboration: Enable non-LCA experts to contribute and review results
Version control: Track changes to models, data, and results
Data confidentiality: Publish the logic to audit the process, not all the data
Parametric & scalable LCA: Automate calculations across scenarios and models
Integration: Connect naKnow's models to other tools, data sources, and workflows
Background DB: Ease the change of background DB, centralize mappings
Why this approach?
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler

## Slide 8
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition activation
Electroless deposition PTH
Electroless deposition etching
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
HCl
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
YAML
description
PATHWAYS

## Slide 9
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition PTH
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
HCl
Electroless deposition etching
Electroless deposition activation
PATHWAYS
Parameter definition

## Slide 10
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition activation
Electroless deposition PTH
Electroless deposition etching
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
HCl
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
BLOCKS
YAML
description

## Slide 11
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition PTH
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
HCl
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
Electroless deposition etching
Electroless deposition activation
BLOCKS
Parametric math formula

## Slide 12
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition activation
Electroless deposition PTH
Electroless deposition etching
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
HCl
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
YAML
description
ELEMENTS
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 13
Input format
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition activation
Electroless deposition PTH
Electroless deposition etching
Previous steps output
Next steps output
Electricity
PdCl2
HCl
Water
Electricity
H2SO4
SnCl2
Water
HCl
Electricity
CuSO4,5H2O
NaH2PO2.H2O
Na3C6H5O7,5.5H2O
H3BO3
NiSO4,7H2O
Water
Other names
Dataset for each background database
ELEMENTS
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets

## Slide 14
LCI compute
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Electroless deposition activation
Electroless deposition etching
Electroless deposition PTH
Electricity
100 mm²
1e-2 g/m²
7 kWh
7 kWh
2e-3 g/m²
5 kWh
3e-3 g/m²
Water
Electricity
Water
Electricity
Water
Water: 1g
Electricity: 7 kWh
Water: 1.3g
Electricity: 14 kWh
Water: 1.5g
Electricity: 19 kWh
Several checks:
- units conversion (Pint)
- allowed mathematical operation (AST)
- other verifications to come
Electricity: 19 kWh
Water:
1.5 g
Total intermediary flows

## Slide 15
LCIA characterization
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Flows
Element mapping
Brightway activity-key demand
Brightway calculation engine
{(database, activity_id) : amount}
Unit conversion
Characterization methods
Impacts results

## Slide 16
Placeholder for main calculator demo
Calculator demo
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler

## Slide 17
Placeholder for main calculator demo
Calculator demo
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler

## Slide 18
Export
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Aggregated flow 1
Aggregated flow n
ES1 XML
Brightway exporter
zip
Block flow 1
Block flow n
Block
ES1 XML
Block flow 1
Block flow l
Block ES1 XML
zip
.
.
.
.
.
.
Aggregated export
Disaggregated export
Brightway exporter
Brightway exporter
.
.
.
.
.
.

## Slide 19
Export
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler

## Slide 20
Collaboration potential
page 4
23/09/2026
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Non-LCA experts: can contribute, build their own models from existing nodes, and compute results
Non-programmers: can build parametric models without coding skills. Conversion from other formats to YAML could be made available.
Version control: Track changes to models, data, and results
Auditability: anyone knowledgable on the modelized device can review the data, propose changes, or build its own version

## Slide 21
Build a transparent, reliable knowledge base
Governance by representants of the supply chain stakeholders, not LCA experts
Provides open methodologies and tools for LCA parametric modelling
The calculator:
  Graph-based built from YAML format, connected to Brightway and background databases
  Favorizes collaborations via human-readable and reviewable by anyone inputs, including non-coders and non LCA experts
page 4
23/09/2026
Conclusion
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Join us!

## Slide 22
Model Correction
page 4
23/09/2026
The initial model estimates elemental fractions from literature and material declarations. ICP tests provide measured fractions for representative samples. The correction keeps the model structure and adds this experimental evidence.
Initial model
estimate and uncertainty
ICP tests
measured fractions and uncertainty
Corrected coefficient
used in the material inventory
+
=
Corrected coefficient =
model weight × model value + Σ(test weight × ICP result)
model weight + Σ test weight
weight = 1 / uncertainty²
A value with lower uncertainty receives more weight. Several ICP samples can contribute to the same corrected coefficient.
After correction
Rescale the remaining fractions so the total composition stays at 100%. Then recalculate the material inventory and environmental impacts to compare the model before and after correction.
naKnow: a collaborative initiative to bridge data gaps in ICT LCA – Marie Reinbigler
Notes: Describe the YAML in short, detailing difference btw element, including the interoperability with other databases/several datasets